AIM:
        Interface two switches and LED’s to Arduino UNO using C++ in ThinkerCad.

SOFTWARE:
        ThikerCad

THEORY:
This project is about working with two LEDs with two PUSH BUTTONs.
For one set of LED and the Push button , when button is pressed LED is set ON and when the button is released, LED will be set OFF. For the other set, it’s the opposite effect.

s1	s2	LED1	LED2
ON	ON	OFF	OFF
ON	OFF	OFF	ON
OFF	ON	ON	OFF
OFF	OFF	ON	ON

Here we represented the working of pushbuttons and switches as,
ON with ‘1’ , OFF with ‘0’

s1	s2	LED1	LED2
1	1	0	0
1	0	0	1
0	1	1	0
0	0	1	1

For LED1

 LED1 = S’1S2 + S’1S’2
        = S’1(S2+S’2)
LED1 = S’1 = LED1 will be on when S1 switch is off

For LED2

 LED2 = S1S’2+S’1S’2
        = S’2 + (S2 +S’1)
LED2 = S’2 = LED2 will be on when S2 switch is off

CIRCUIT:

CODE:

// C++ code
//
int buttonState = 0;

int unnamed = 0;

int i = 0;

void setup()
{
  pinMode(2, INPUT);
  pinMode(13, OUTPUT);
  pinMode(3, INPUT);
  pinMode(12, OUTPUT);
}

void loop()
{
  buttonState = digitalRead(2);
  if (buttonState == HIGH) {
    digitalWrite(13, LOW);
  } else {
    digitalWrite(13, HIGH);
  }
  buttonState = digitalRead(3);
  if (buttonState == HIGH) {
    digitalWrite(12, LOW);
  } else {
    digitalWrite(12, HIGH);
  }

  buttonState == HIGH;
  delay(10); // Delay a little bit to improve simulation performance
}

RESULT:

        Interface two switches and LEDs to Arduino UNO using C++ is done.